## Slide 1
Switching Concepts
VLAN, TRUNK, DTP, VTP, Port Security

## Slide 2
Switching Concepts
What is Switch?
HUB
Bridge
Switch
Collision Domain
Broadcast Domain
CSMA/CD
Interface characteristic
Speed
Duplex

## Slide 3
Packet Forwarding
Ethernet (IEEE 802.3)
MAC address
Store and Forward
Cut Through
Fragment free
Packet Types
Unicast
Broadcast
Unknown unicast
Preamble | SOF | DMAC | SMAC | Type/Length | DSAP | SSAP | Control | Data | FCS
7 | 1 | 6 | 6 | 2 | 1 | 1 | 2 | 46~1500 | 4
802.3x (1997)
802.2
Switching Concepts
CCNA (Cisco Certified Network Associate)

## Slide 4
Switching Components
Content Addressable Memory (CAM)
Ternary Content Addressable Memory (TCAM)
Forwarding Information Base (FIB)
Switching Concepts

## Slide 5
Switch Types
Layer 2 Switches
Multilayer Switches
Modular Multilayer Switches
Switch Modules
Supervisor Engine
Line Cards
SFP
GBIC
Switching Concepts

## Slide 6
Ethernet Technology
Ethernet (IEEE 802.3) (10Mbps)
Fast Ethernet (IEEE 802.3u) (100Mbps)
Gigabit Ethernet (IEEE 802.3z , 802.3ab) (1Gbps)
10Gigabit Ethernet (IEEE 802.3ae, 802.3an) (10Gbps)
Switch Modules
SFP
GBIC
XENPAK
X2
SFP+
Switching Concepts

## Slide 7
What is LAN?
Same Broadcast Domain
Same Subnet
Switching Concepts

## Slide 8
What is LAN?
Same Broadcast Domain
Same Subnet
Switching Concepts

## Slide 9
What is VLAN?
Same Broadcast Domain
Same Subnet
Switching Concepts

## Slide 10
VLAN Benefits
Security
Reduce Broadcast Domain
Flexibility and Scalability
Switching Concepts

## Slide 11
VLAN Membership
Static
Dynamic (VMPS)
Voice VLAN
Switching Concepts

## Slide 12
TRUNK
ISL (Inter Switch Link)
802.1Q
Switching Concepts

## Slide 13
ISL (Inter Switch Link)
Cisco Proprietary
26 Byte Header
4 Byte CRC
VLAN ID
Support 4094 VLANs
1 – 1005 = Normal Range
>1005 = Extended Range
Switching Concepts

## Slide 14
802.1Q
ISO Standard
4 Byte Tag
VLAN ID
Support 4094 VLANs
1 – 1005 = Normal Range
>1005 = Extended Range
Native VLAN
Switching Concepts

## Slide 15
DTP (Dynamic Trunking Protocol)
Dynamic Mode
Desirable
Auto
Switching Concepts

## Slide 16
VTP (VLAN Trunking Protocol)
VTP Domain
VTP Mode
  Server
  Client
  Transparent
VTP Password
Switching Concepts

## Slide 17
Inter VLAN Routing
Router on a stick
Subinterface
Inter VLAN Routing
Interface Vlan
Switching Concepts

## Slide 18
Inter VLAN Routing
Router on a stick
Subinterface
Inter VLAN Routing
Interface Vlan
Switching Concepts

## Slide 19
Port Security
Violation:
1- Shutdown
2- Restrict
3- Protect
Switching Concepts

## Slide 20
Switching Basic
Switching Concepts